## Slide 1
ECE 281 Lesson 29
1

## Slide 2: Lab3 – Due Friday
How is it going?

## Slide 3: Lesson 29 Outline
Do Time Logs!
Review
Assembly
Assembly to Machine Code

## Slide 4: Architecture vs Micro-Architecture
Architecture: the programmer’s view of the computer
  Defined by instruction set and operand locations (i.e. registers, instructions, and memory)
  Types – x86, PowerPC, ARM, and MIPS
Micro-architecture: how to implement an architecture in hardware – Pentium, A10
  Specific arrangement of registers, memories, ALUs etc.
  Many different microarchitectures exist for a single architecture

## Slide 5
Computer Block Diagram
CPU
Control
Datapath
ALU
Memory
Input/
Output
Control Bus
Data Bus
Address Bus
Outside
World

## Slide 6: Components of Computer Architecture
1) CPU – Central Processing Unit
  Controller – makes other components work together
  Datapath – does computations; keep track of where we are. What are we tracking?
    Program Counter
2) Memory – Stores information (code and data)
  Address – where info is located
  Data – what info is
3) I/O – data goes in/out to/from the outside world

## Slide 7
Figure 6.1 Word-addressable memory
Copyright © 2013 Elsevier Inc. All rights reserved.
Addressable Memory
width =
width = 1 word (32-Bits)

## Slide 8: CISC vs RISC
RISC
  Reduced Instruction Set Computer
CISC
  Complex Instruction Set Computer
Tradeoffs RISC vs CISC
  more instructions == more complex hardware
Complex
SW
Complex
HW

## Slide 9
Figure 6.4 Big-endian and little-endian data storage
Copyright © 2013 Elsevier Inc. All rights reserved.
Big-Endian vs Little-Endian
Big-Endian – Byte numbering starts @ MSB
Little-Endian – Byte numbering starts @ LSB

## Slide 10: MIPS Architecture
The MIPS Architecture consists of:
  A set of operations (instructions)
    I-Type, R-Type, J-Type
  Data units (sizes, addressing modes, etc.)
    32-Bit Data Word
  Registers
    32, 32-bit registers
  Interaction with memory
    Harvard Architecture
    Load and Store
  Program counter
    32-bit PC
Is MIPS byte-addressable or word-addressable memory?
Is MIPS Little-Endian or Big-Endian?
Is MIPS RISC or CISC?

## Slide 11: Compiler/Assembler Translation
Translating a Program to Machine Code
Compiler
Assembler
Higher Level Language (HLL)
Assembly Language
Machine Code

## Slide 12: Assembly Code

## Slide 13: Assembly Code

## Slide 14: Assembly Code
Mnemonic – name of an operation/instruction
Opcode – binary representation of mnemonic
Operand – target of operation/instruction
  lw $s3, 4($0)
   100011 (found in Appendix B of book)
MIPS Architecture:
  $ indicates a register
  32 Registers
  32 bits in a word
  $0 $t $s
Mnemonic
Operands
Opcode

## Slide 15
Copyright © 2013 Elsevier Inc. All rights reserved.
MIPS Register Set
We will focus in 281 on these, but 382 will do more

## Slide 16: Lab 4
These will be registers in our MIPS processor
Mnemonic

## Slide 17
J-Type | 
op | 
6 bits | 
R-Type |  |  |  |  | 
op |  |  |  |  | 
6 bits |  |  |  |  | 
R-Type |  |  |  |  | 
op | rs | rt | rd | shamt | funct
6 bits | 5 bits | 5 bits | 5 bits | 5 bits | 6 bits
I-Type |  |  | 
op |  |  | 
6 bits |  |  | 
MIPS Instruction Types
I-Type |  |  | 
op | rs | rt | imm
6 bits | 5 bits | 5 bits | 16 bits
J-Type | 
op | addr
6 bits | 26 bits
R-Type Instructions – Register Type
I-Type Instructions – Immediate Type
J-Type Instructions – Jump Type

## Slide 18
MIPS Instruction Set
Copyright © 2013 Elsevier Inc. All rights reserved.
Table B.1 Instructions, sorted by opcode

## Slide 19
MIPS Instruction Set
Copyright © 2013 Elsevier Inc. All rights reserved.
Table B.1 Instructions, sorted by opcode

## Slide 20
MIPS Instruction Set
Copyright © 2013 Elsevier Inc. All rights reserved.
Table B.2 R-type instructions, sorted by funct field

## Slide 21
MIPS Instruction Set
Copyright © 2013 Elsevier Inc. All rights reserved.
Table B.2 R-type instructions, sorted by funct field

## Slide 22
MIPS Instruction Set
Copyright © 2013 Elsevier Inc. All rights reserved.
Table B.3 F-type instructions (fop = 16/17)

## Slide 23
R-Type Instructions
R-Type |  |  |  |  | 
op | rs | rt | rd | shamt | funct
6 bits | 5 bits | 5 bits | 5 bits | 5 bits | 6 bits
R-Type Instructions – Register Type
Uses 3 registers operands (2 source, 1 destination)
Example Assembly Instruction: instr rd, rs, rt
Ex: add $t0, $s4, $s5
Source
Destination

## Slide 24
R-Type Instructions
You Try:
Ex: add $s0, $s1, $s2
Ex: sub $t0, $t3, $t5

## Slide 25
I-Type Instructions
I-Type |  |  | 
op | rs | rt | imm
6 bits | 5 bits | 5 bits | 16 bits
I-Type Instructions – Immediate Type
Uses 2 registers operands and 1 immediate operand
Example Assembly Instruction:
instr rt, rs, imm
instr rd, imm (rs)
Ex: addi $s3, $s3, 4

## Slide 26
26

## Slide 27
Bit Masking
Given: A = 0x12345678
B = 0xFFFF0000
What is A AND B (AB)?
What is A OR B (A+B)?
AND – clear bits
OR – set bits

## Slide 28
Copyright © 2013 Elsevier Inc. All rights reserved.
Figure 6.9 Machine code for I-type instructions
I-Type Instructions

## Slide 29
Copyright © 2013 Elsevier Inc. All rights reserved.
Figure 6.10 Machine code for an l-type instruction
I-Type Instructions

## Slide 30
Copyright © 2013 Elsevier Inc. All rights reserved.
J-Type Instructions
J-Type | 
op | addr
6 bits | 26 bits
J-Type Instructions – Jump Type
j or jal (jr is an R-Type Instruction that uses only the rs operand)
26 Bits for the Target or offset value  Pseudo-Direct Addressing
New address is computed by taking the upper 4 bits of the PC, concatenated to the 26 bit immediate value, and the lower two bits are 00, so the address created remains word-aligned. PC <- PC31-28 & IR25-0 & 00

## Slide 31
Copyright © 2013 Elsevier Inc. All rights reserved.
J-Type Instructions
J-Type | 
op | addr
6 bits | 26 bits
Given this code convert Jump:
0x00400000 addi $s0, $0, 4 # $s0 = 4
0x00400004 addi $s1, $0, 1 # $s1 = 1
0x00400008 j target # jump to target
0x0040000c addi $s1, $s1, 1 # not executed
0x00400010 sub $s1, $s1, $s0 # not executed
target:
0x00400014 add $s1, $s1, $s0 # $s1 = 1 + 4 = 5

## Slide 32
Copyright © 2013 Elsevier Inc. All rights reserved.
Figure 6.12 Machine code to assembly code translation
More Instructions

## Slide 33
Machine Code to Assembly
Find the Assembly Function:
Given Machine Code: 0xAD310004

## Slide 34
Copyright © 2013 Elsevier Inc. All rights reserved.
MIPS Register Set

## Slide 35
MIPS Instruction Set
Copyright © 2013 Elsevier Inc. All rights reserved.
Table B.1 Instructions, sorted by opcode

## Slide 36
MIPS Instruction Set
Copyright © 2013 Elsevier Inc. All rights reserved.
Table B.1 Instructions, sorted by opcode

## Slide 37
MIPS Instruction Set
Copyright © 2013 Elsevier Inc. All rights reserved.
Table B.2 R-type instructions, sorted by funct field

## Slide 38
MIPS Instruction Set
Copyright © 2013 Elsevier Inc. All rights reserved.
Table B.2 R-type instructions, sorted by funct field

## Slide 39
MIPS Instruction Set
Copyright © 2013 Elsevier Inc. All rights reserved.
Table B.3 F-type instructions (fop = 16/17)

## Slide 40
Copyright © 2013 Elsevier Inc. All rights reserved.
Figure 6.5 R-type machine instruction format
Figure 6.8 I-type instruction format
Figure 6.11 J-type instruction format
MIPS Instruction Types
Register
Immediate
Jump

## Slide 41
Copyright © 2013 Elsevier Inc. All rights reserved.
MIPS Register Set

## Slide 42
Copyright © 2013 Elsevier Inc. All rights reserved.
MIPS Register Set

## Slide 43
Copyright © 2013 Elsevier Inc. All rights reserved.
Figure 6.7 Machine code for the R-type instruction of Example 6.3
R-Type Instructions