## Slide 1
ECE 281 Lesson 11
1
Maj Walchko

## Slide 2
ALU – Block Diagram
ALU: Arithmetic Logic Unit
  Combine Math and Logic
  Heart of most computers
  Has 7 functions
Control Signals |  |  | 
F2 | F1 | F0 | Y
0 | 0 | 0 | A and B
0 | 0 | 1 | A or B
0 | 1 | 0 | A + B
0 | 1 | 1 | Not Used
1 | 0 | 0 | A and B’
1 | 0 | 1 | A or B’
1 | 1 | 0 | A – B
1 | 1 | 1 | set <

## Slide 3
ALU – Block Diagram
Build an ALU with logic Functions:
What do we need?
  Adder
  Inverter
  And
  Or
  Mux
  Comparator
How would we design this? Let’s draw it out …
Control Signals |  |  | 
F2 | F1 | F0 | Y
0 | 0 | 0 | A and B
0 | 0 | 1 | A or B
0 | 1 | 0 | A + B
0 | 1 | 1 | Not Used
1 | 0 | 0 | A and B’
1 | 0 | 1 | A or B’
1 | 1 | 0 | A – B
1 | 1 | 1 | set <

## Slide 4
ALU

## Slide 5
Multiplication in Binary
An ALU can add and subtract in binary
How do we multiply in Binary?
 |  | 1 | 0 | 1 |  |  | 
 | X | 0 | 1 | 1 |  | X | 
 |  |  |  |  |  |  | 
By adding and shifting, we can multiply numbers

## Slide 6: Shift Summary
 | Right | Left
Logical Shift | Always 0 | Always 0
Arithmetic Shift | Always MSB | Always 0
 | Right | Left
Logical Shift |  | 
Arithmetic Shift |  | 
Shifter:
  Logical Shift Right/Left – fill empty spots with 0’s
  Arithmetic Shift Right (ASR) – when shifting right, fills empty spots with MSB (to preserve sign)
  ASL is same as LSL

## Slide 7
Rotator
Rotator:
  SHIFT from one end to the other
  # that falls off one end attaches to other end
0 0 0 1 0
1 0 1 0 0
0 0 1 0
0 0 1 0

## Slide 8
Shamt
Shamt:
  Shift Amount
Why is this useful?
  Helps multiply and divide!

## Slide 9
Examples
100110  Logical Shift Right 
What if it was an Arithmetic Shift Right on a signed number?
100110  Arithmetic Shift Right 
100110  Logical/Arithmetic Shift Left (6-Bit System) 
00100110  Logical/Arithmetic Shift Left (8-Bit System)

## Slide 10
Practice
Practice:
Use Only two 2:1 mux to create a 3:1 mux:

## Slide 11
Quiz
Quiz: 5 Min
http://www.online-stopwatch.com/full-screen-stopwatch/

## Slide 12
12

## Slide 13
Shifter
Shifter:
  Logical Shift Right/Left – fill empty spots with 0’s
  Arithmetic Shift Right (ASR) – when shifting right, fills empty spots with MSB (to preserve sign)
  ASL is same as LSL