## Slide 1
ECE 281 Lesson 14
1

## Slide 2: Lesson 14 Outline
Do Time Logs!
Sequential Circuits
SR Latch
D Latch
D Flip Flop
Register

## Slide 3: Sequential Circuits
Introduction to Sequential Circuits
  Combinational Logic – Outputs depend on current inputs
  Sequential Logic – Outputs depend on current and prior inputs
     i.e. has memory

## Slide 4: Cross Coupled Inverter
Figure 3.1 Cross-coupled inverter pair

## Slide 5: SR Latch
Simplest Sequential Circuit
Copyright © 2013 Elsevier Inc. All rights reserved.
Figure 3.3 SR latch schematic
Figure 3.6 SR latch symbol

## Slide 6: SR Latch
Simplest Sequential Circuit
S = Set
R = Reset
Q = Stored Value
PROBLEM 1) Q changes whenever an input changes
* Undefined… Q and Q’ can’t both be 0
Figure 3.3 SR latch schematic
S | R | Q | 
S | R | Q | 
Biggest problem is when S + R are both 1
S | R | Q | 
1 | 0 | 1 | 0
0 | 0 | Qprev | 
0 | 1 | 0 | 1
0 | 0 | Qprev | 
1 | 1 | 0 | 0*
S | R | Q | 
1 | 0 | 1 | 0
0 | 0 | Qprev | 
0 | 1 | 0 | 1
0 | 0 | Qprev | 
1 | 1 | 0 | 0*

## Slide 7: D-Latch
Solves the problem of the SR Latch when both S & R are asserted
C = Control/Clock
D = Data
Q = Stored value
Q changes whenever C is high and D changes
Problem?
Copyright © 2013 Elsevier Inc. All rights reserved.
Figure 3.7 D latch: (a) schematic, (b) truth table, (c) symbol
C | D | Q | 
C | D | Q | 
C | D | Q | 
1 | 0 | 1 | 0
0 | 0 | Qprev | 
0 | 1 | 0 | 1
C | D | Q | 
1 | 0 | 1 | 0
0 | 0 | Qprev | 
0 | 1 | 0 | 1
Problem with D latch: What if we don’t always want D to update?

## Slide 8: D-Latch
transparent – if C is high, Q will follow input (D) (i.e. D flows through)
opaque – if C is low, Q won’t change (i.e. D doesn’t flow through)
Copyright © 2013 Elsevier Inc. All rights reserved.
Figure 3.7 D latch: (a) schematic, (b) truth table, (c) symbol

## Slide 9: D-Flip Flop
D Flip-Flop – Two D-Latches back to back with complementary clocks in a Master/Slave Configuration
  CLK = Clock
  D = Data
  Q = Stored Value
CLK | D | Q | 
CLK | D | Q | 
Copyright © 2013 Elsevier Inc. All rights reserved.
Figure 3.8 D flip-flop: (a) schematic, (b) symbol, (c) condensed symbol
CLK | D | Q | 
0 | 0 | Qprev | 
0 | 1 | Qprev | 
1 | 0 | Qprev | 
1 | 1 | Qprev | 
↑ | 0 | 0 | 1
↑ | 1 | 1 | 0
CLK | D | Q | 
0 | 0 | Qprev | 
0 | 1 | Qprev | 
1 | 0 | Qprev | 
1 | 1 | Qprev | 
↑ | 0 | 0 | 1
↑ | 1 | 1 | 0

## Slide 10: D-Flip Flop
Called an edge-trigged device
Q changes when clock changes
Enabled flip-flop – Add EN signal to determine if data will load on edge
Resettable flip-flop – resets output to 0 when reset enabled. Useful for hearing known states
Copyright © 2013 Elsevier Inc. All rights reserved.
Figure 3.8 D flip-flop: (a) schematic, (b) symbol, (c) condensed symbol

## Slide 11: D-Flip Flop vs D-Latch
*What is the difference between a latch and a flip flop?
  A Flip Flop changes on the clock edge a latch changes at any time
    D-Latch updates it’s state continuously while clk = ‘1’
    Copies D  Q on Rising Edge of Clock and remembers it’s state on all others

## Slide 12: Register
Copyright © 2013 Elsevier Inc. All rights reserved.
Register
  An N-Bit Register is a Bank of N-Flip Flops
Figure 3.9 A 4-bit register: (a) schematic and (b) symbol

## Slide 13: Example Waveform
FF
Latch
(clk falling)
(clk = 0)

## Slide 14: Synchronous Circuit Properties
Synchronous circuit – Combinational circuit followed by bank of flip flops
  Properties:
  Each element is either a register or a combinational circuit
  At least one circuit is a register
  All registers have the same clock
  Every cyclic path contains at least one register
  Example: FSMs, Pipelines
Asynchronous circuit – Sequential circuits without a clock
  Timing not limited by clock registers

## Slide 15: Examples of Circuits
Example 3.5: Synchronous Sequential Circuits
Copyright © 2013 Elsevier Inc. All rights reserved.
Figure 3.21 Example circuits

## Slide 16
16

## Slide 17: Cross Coupled Inverter
Figure 3.2 Bistable operation of cross-coupled inverters

## Slide 18: SR Latch
Copyright © 2013 Elsevier Inc. All rights reserved.
Figure 3.4 Bistable states of SR latch

## Slide 19: SR Latch
Copyright © 2013 Elsevier Inc. All rights reserved.
Figure 3.5 SR latch truth table

## Slide 20: Example Waveform
Copyright © 2013 Elsevier Inc. All rights reserved.
Figure 3.14 Example waveforms

## Slide 21: Example Waveform
Copyright © 2013 Elsevier Inc. All rights reserved.
Figure 3.15 Solution waveforms