## Slide 1
ECE 281 Lesson 15
1
Maj Walchko

## Slide 2: Lesson 15 Outline
Do Time Logs!
Homework #2 (LSN 15/16 Worksheet) Due LSN 17
Lab #2 Prelab Due LSN 19
Finite State Machines – FSMs
  Design FSMs

## Slide 3: CE3
c_B_mux2
c_result
Define intermediate signals (wires)
Just a piece of the code … behavioral
Don’t forget to add 3 more test vectors of your own!!
Use comments to explain what is happening

## Slide 4: D-Flip Flop
CLK | D | Q | 
0 | 0 | Qprev | 
0 | 1 | Qprev | 
1 | 0 | Qprev | 
1 | 1 | Qprev | 
↑ | 0 | 0 | 1
↑ | 1 | 1 | 0
CLK | D | Q | 
0 | 0 | Qprev | 
0 | 1 | Qprev | 
1 | 0 | Qprev | 
1 | 1 | Qprev | 
↑ | 0 | 0 | 1
↑ | 1 | 1 | 0
Copyright © 2013 Elsevier Inc. All rights reserved.
Figure 3.8 D flip-flop: (a) schematic, (b) symbol, (c) condensed symbol

## Slide 5: Flip-Flops
From last time: What do F/Fs create?
  Memory!
When do F/Fs this?
  Clock Edge!
Copyright © 2013 Elsevier Inc. All rights reserved.
Figure 3.20 Flip-flop current state and next state

## Slide 6: Synchronous Circuit Properties
Synchronous circuit – Combinational circuit followed by bank of flip flops
  Properties:
  Each element is either a register or a combinational circuit
  At least one circuit is a register
  All registers have the same clock
  Every cyclic path contains at least one register
  Example: FSMs, Pipelines
Asynchronous circuit – Timing not limited by clock registers

## Slide 7: Examples of Circuits
Example 3.5: Synchronous Sequential Circuits
Each element is either a register or a combinational circuit
At least one circuit is a register
All registers have the same clock
Every cyclic path contains at least one register
Notes: Solutions
Circuit:
(a) is combinational, not sequential, because it has no registers.
(b) is a simple sequential circuit with no feedback.
(c) is neither a combinational circuit nor a synchronous sequential circuit, because it has a latch that is neither a register nor a combinational circuit.
(d) and (e) are synchronous sequential logic; they are two forms of finite state machines, which are discussed in Section 3.4.
Same as (d)
(f) is neither combinational nor synchronous sequential, because it has a cyclic path from the output of the combinational logic back to the input of the same logic but no register in the path.
(g) is synchronous sequential logic in the form of a pipeline, which we will study in Section 3.6.
(h) is not, strictly speaking, a synchronous sequential circuit, because the second register receives a different clock signal than the first, delayed by two inverter delays.

## Slide 8: Finite State Machines
Robot
TCP

## Slide 9: Simple Coin-operated Turnstile

## Slide 10: Finite State Machines
FSM – M- inputs, N – Outputs, and K - bits of state
  FSMs have K registers that can be one of a finite number (2K) unique states
Two types of FSMs
  Moore FSM
  Mealy FSM
Combinational Logic or
Next State Logic
Flip Flops
Output Logic
Inputs
Outputs
Current
State
Next
State
Clock
M
K
K
N

## Slide 11: Finite State Machines - Moore Machine
Moore Machine – outputs depend only on current state of the machine.
Combinational Logic or
Next State Logic
Flip Flops
Output Logic
Inputs
Outputs
Current
State
Next
State
Clock
M
K
K
N
S1
Out=1
S0
Out=0
C=1
In = 0
In =1
In = 0
Random
Ex FSM

## Slide 12: Finite State Machines - Mealy Machine
Mealy Machine – outputs depend on both the current state and current inputs of the machine.
Combinational Logic or
Next State Logic
Flip Flops
Output Logic
Inputs
Outputs
Current
State
Next
State
Clock
M
K
K
N
S1
S0
In = 0
Out = 1
In =1
Out = 0
In = 0
Out = 1
Random
Ex FSM

## Slide 13: Finite State Machines - Design
How to Design a State Machine:
  0) Description
  1) State Transition Diagram
  2) State Transition Table & Output Table
  3) Next State and Output State Equations
  4) Schematic
Lets Build a Vending Machine:
  Only takes Quarters. Only sells Root Beer (RB)
  No change. 50₵ per Soda
  Inputs: C = Coin (also, there’s a clock)
  Outputs: S = Soda
Copyright © 2013 Elsevier Inc. All rights reserved.
Real Life Examples of State Machines:
Soda Machine
Software Applications
Spell Checker – Using Soundex
Driving to School/Work

## Slide 14: Finite State Machines - Moore vs Mealy Machine
Moore Machine – outputs depend only on current state of the machine.
Mealy Machine – outputs depend on both the current state and current inputs of the machine.
Combinational Logic or
Next State Logic
Flip Flops
Output Logic
Inputs
Outputs
Current
State
Next
State
Clock
M
K
K
N
Combinational Logic or
Next State Logic
Flip Flops
Output Logic
Inputs
Outputs
Current
State
Next
State
Clock
M
K
K
N

## Slide 15: In-Class Exercise
Draw me a picture of a Mealy or Moore State Transition Diagram that shows
A Snail is crawling across a sequence of numbers and he smiles if the last 2 numbers are “11”
Sequence: 0100110111

## Slide 16: In-Class Exercise – One Moore Solution
A Snail is crawling across a sequence of numbers and he smiles if the last 2 numbers are “11”
Sequence: 0100110111
S1
=0
S0
=0
S3
=1
N=0
N=1
N=1
N=0
N=0
N=1
reset

## Slide 17
17

## Slide 18
S1
$0.25
RB=0
S0
$0
RB=0
S2
$0.50
RB=1
C=1
C=0
C=1
C=X

## Slide 19
Moore FSM
Mealy FSM

## Slide 20: Finite State Machines - Moore vs Mealy Machine
S1
25₵
T=0
S0
0₵
T=0
S3
50₵
T=1
GreenR=0
G=1
Y=0
Red
R=1
G=0
Y=0
Yellow
R=0
G=0
Y=1
S2
T=0
Ghost State
C=0
C=1
C=0
C=1
C=X

## Slide 21: Homework – Review Book Example
Take a look at how the book implements “01”
Example 3.7 on p 132
A Snail is crawling across a sequence of numbers and he smiles if the last 2 numbers are “01”
Sequence: 0100110111

## Slide 22: Homework – Review Book Example
Example 3.7 on p 132
A Snail is crawling across a sequence of numbers and he smiles if the last 2 numbers are “01”
Sequence: 0100110111
Copyright © 2013 Elsevier Inc. All rights reserved.
Figure 3.30 FSM state transition diagrams: (a) Moore machine, (b) Mealy machine