## Slide 1
ECE 281 Lesson 16
1

## Slide 2: Lesson 16 Outline
Do Time Logs!
Homework #2 (LSN 15/16 Worksheet) Due LSN 17 (next time)
Lab #2 Prelab Due LSN 19
A little Review
Finite State Machines – FSMs
  FSM Analysis

## Slide 3: Review: Flip-Flops
From last time: What do F/Fs create?
  Memory!
When do F/Fs this?
  Clock Edge!
Copyright © 2013 Elsevier Inc. All rights reserved.
Figure 3.20 Flip-flop current state and next state

## Slide 4: Finite State Machines - Moore vs Mealy Machine
Moore Machine – outputs depend only on current state of the machine.
Mealy Machine – outputs depend on both the current state and current inputs of the machine.
Combinational Logic or
Next State Logic
Flip Flops
Output Logic
Inputs
Outputs
Current
State
Next
State
Clock
M
K
K
N
Combinational Logic or
Next State Logic
Flip Flops
Output Logic
Inputs
Outputs
Current
State
Next
State
Clock
M
K
K
N

## Slide 5: Question 1
True/False The state transition diagram below represents a Moore machine.

## Slide 6: Questions 2 & 3
Is the finite state machine below a Mealy or Moore machine?
What is the next state equation for D1?
D1
D2

## Slide 7: Question 4
For the finite state machine below, if the state machine is in state S2 and the input EN is a '1' when the clock transitions from low to high, what will be the machine's next state and output?
Current State S | Input EN | Next State S’ | Output Y
S0 | 0 | S0 | 0
S0 | 1 | S1 | 0
S1 | 0 | S0 | 1
S1 | 1 | S2 | 1
S2 | 0 | S3 | 1
S2 | 1 | S2 | 0
S3 | 0 | S0 | 0
S3 | 1 | S1 | 1

## Slide 8: Questions 5 & 6 & 7
True/False The steps for designing a clocked synchronous state machine, starting from a word description, are just about the reverse of the analysis steps.
If a state machine requires 5 states to implement the problem, how many D flip-flops are needed (assume binary encoding)?
If a state machine requires 5 states to implement the problem, how many total states will exist in the final circuit?

## Slide 9: Question 8
Which of these circuits is a valid synchronous sequential circuit?
  Synchronous Sequential Circuit Properties:
  Each element is either a register or a combinational circuit
  At least one circuit is a register
  All registers have the same clock
  Every cyclic path contains at least one register

## Slide 10: Reverse Engineering

## Slide 11: Finite State Machines – Design/Analysis
State Machines:
  0) Description
  1) State Transition Diagram
  2) State Transition Table & Output Table
  3) Next State and Output State Equations
  4) Schematic
Copyright © 2013 Elsevier Inc. All rights reserved.
Design
Analysis

## Slide 12: Finite State Machines – Analysis Joe Homeowner’s Garage Door Opener
Joe Homeowner’s Gargage Door Opener…we are given the schematic
Copyright © 2013 Elsevier Inc. All rights reserved.
S1
S1
S0
S0
A0
A1
CLK
CLK
MSB
LSB
S0
S1*
S0*
A0
A1

## Slide 13: Finite State Machines – Analysis Joe Homeowner’s Garage Door Opener
Next State Table: |  |  |  |  |  | 
Current State |  | Inputs |  | Next State |  | Next State Name
S1 | S0 | A1 | A0 | S1* | S0* | 
0 | 0 | 0 | 0 |  |  | 
0 | 0 | 0 | 1 |  |  | 
0 | 0 | 1 | 0 |  |  | 
0 | 0 | 1 | 1 |  |  | 
0 | 1 | 0 | 0 |  |  | 
0 | 1 | 0 | 1 |  |  | 
0 | 1 | 1 | 0 |  |  | 
0 | 1 | 1 | 1 |  |  | 
1 | 0 | 0 | 0 |  |  | 
1 | 0 | 0 | 1 |  |  | 
1 | 0 | 1 | 0 |  |  | 
1 | 0 | 1 | 1 |  |  | 
1 | 1 | 0 | 0 |  |  | 
1 | 1 | 0 | 1 |  |  | 
1 | 1 | 1 | 0 |  |  | 
1 | 1 | 1 | 1 |  |  | 
Output Table |  |  | 
Current State |  | Output | State Name
S1 | S0 | Unlock | 
Step 4) Schematic
Step 2) State Transition Table & Output Table

## Slide 14: Finite State Machines – Analysis Joe Homeowner’s Garage Door Opener
Next State Table: |  |  |  |  |  | 
Current State |  | Inputs |  | Next State |  | Next State Name
S1 | S0 | A1 | A0 | S1* | S0* | 
0 | 0 | 0 | 0 | 0 | 0 | M0
0 | 0 | 0 | 1 | 0 | 0 | M0
0 | 0 | 1 | 0 | 0 | 0 | M0
0 | 0 | 1 | 1 | 0 | 1 | M1
0 | 1 | 0 | 0 | 0 | 0 | M0
0 | 1 | 0 | 1 | 1 | 0 | M2
0 | 1 | 1 | 0 | 0 | 0 | M0
0 | 1 | 1 | 1 | 0 | 0 | M0
1 | 0 | 0 | 0 | 0 | 0 | M0
1 | 0 | 0 | 1 | 0 | 0 | M0
1 | 0 | 1 | 0 | 0 | 0 | M0
1 | 0 | 1 | 1 | 0 | 0 | M0
1 | 1 | 0 | 0 | 0 | 0 | N/A
1 | 1 | 0 | 1 | 1 | 0 | N/A
1 | 1 | 1 | 0 | 0 | 0 | N/A
1 | 1 | 1 | 1 | 0 | 0 | N/A
Step 1) State Transition Diagram
M0
M1
M2
M3 Ghost State – never gets here
Step 2) State Transition Table & Output Table
Output Table |  |  | 
Current State |  | Output | State Name
S1 | S0 | Unlock | 
0 | 0 | 0 | M0
0 | 1 | 0 | M1
1 | 0 | 1 | M2
1 | 1 | 1 | M3
Step 0) Description
What is the Door combination?
reset
M3
Unlock=1
Ghost
State
M0
Unlock=0
else
M1
Unlock=0
A=11(3)
else
M2
Unlock=1
A=01(1)
any A

## Slide 15: Finite State Machines – Analysis Joe Homeowner’s Garage Door Opener
reset
M3
Unlock=1
Ghost
State
M0
Unlock=0
else
M1
Unlock=0
A=11(3)
else
M2
Unlock=1
A=01(1)
any A

## Slide 16: Another Analysis Example HW 3.31
HW 3.31 – Write the next state/output tables and equations. Draw the state transition diagram.
S1
S0
S1*
S0*
MSB
LSB

## Slide 17: Another Analysis Example HW 3.31
Next State Table: |  |  |  |  | 
Current State |  | Inputs | Next State |  | Next State
S1 | S0 | X | S1* | S0* | Name
Step 4) Schematic
Step 3) Next State and Output State Equations
Next State Equations
Output Equation:
Step 2) State Transition Table & Output Table
Output Table |  |  | 
Current State |  | Output | State Name
S1 | S0 | Q | 
Step 3) Next State and Output State Equations
Next State Equations
Output Equation:
M0
M1
M2
M3

## Slide 18: Another Analysis Example HW 3.31
Step 2) State Transition Table & Output Table
M0
M1
M2
M3
Output Table |  |  | 
Current State |  | Output | State Name
S1 | S0 | Q | 
0 | 0 | 0 | M0
0 | 1 | 1 | M1
1 | 0 | 1 | M2
1 | 1 | 1 | M3
Next State Table: |  |  |  |  | 
Current State |  | Inputs | Next State |  | Next State
S1 | S0 | X | S1* | S0* | Name
0 | 0 | 0 | 1 | 0 | M2
0 | 0 | 1 | 1 | 1 | M3
0 | 1 | 0 | 1 | 0 | M2
0 | 1 | 1 | 1 | 0 | M2
1 | 0 | 0 | 0 | 0 | M0
1 | 0 | 1 | 0 | 1 | M1
1 | 1 | 0 | 1 | 0 | M2
1 | 1 | 1 | 1 | 0 | M2
Step 1) State Transition Diagram
Step 0) Description
Step 0) Description
This finite state machine is a divide-by-two counter (see Section 3.4.2) when X = 0. When X = 1, the output, Q, is HIGH.
M0
Q=0
M1
Q=1
M2
Q=1
X=X
X=1
M3
Q=1
X=X
X=1
X=0
X=0

## Slide 19: Divide-by-N Counter – Example 3.6
Has one output and no inputs
The output Y is HIGH for one clock cycle out of every N
In other words, the output divides the frequency of the clock by N

## Slide 20: Divide-by-3 Counter – Example 3.6
The waveform and state transition diagram for a divide-by-3 counter is shown in Figure 3.28
Next State Table | 
Current State | Next State
S0 | S1
S1 | S2
S2 | S0
Output Table | 
Current State | Output
S0 | 1
S1 | 0
S2 | 0

## Slide 21: Another Analysis Example
HW 3.31 – Write the next state/output tables and equations. Draw the state transition diagram.
S1
S0
S1*
S0*

## Slide 22
22

## Slide 23: Question 9
State machine analysis is a process that begins with a circuit schematic and results in a state transition diagram. If given a schematic, the first step in analysis would be:
  Determine the logic elements required to build the state machine
  Determine the next-state and output functions implemented by the circuit
  Predict the next state that the circuit will transition to

## Slide 24: AIM-9B AA-2 (K-13)

## Slide 25: F-35 / J-31
http://www.airliners.net/photo/Untitled-(AVIC)/Shenyang-J-31-(F60)/2542713/L/
By U.S. Air Force photo by Master Sgt. Donald R. Allen - http://www.dvidshub.net/image/935698/aerial-refueling-f-35-lightning-ii-joint-strike-fighters-eglin-afb-fla#.UZyEMrVU8QY, Public Domain, https://commons.wikimedia.org/w/index.php?curid=49689165

## Slide 26: Finite State Machines – Analysis Joe Homeowner’s Garage Door Opener
Next State Table: |  |  |  |  |  | 
Current State |  | Inputs |  | Next State |  | Next State Name
S1 | S0 | A1 | A0 | S1* | S0* | 
Output Table |  |  | 
Current State |  | Output | State Name
S1 | S0 | Unlock | 
Step 3) Next State and Output State Equations
Next State Equations
Output Equation:
Step 4) Schematic
Step 2) State Transition Table & Output Table
Step 3) Next State and Output State Equations
Next State Equations
Output Equation:

## Slide 27: In-Class Exercise
Draw me a picture of a Mealy or Moore State Transition Diagram that shows
A Snail is crawling across a sequence of numbers and he smiles if the last 2 numbers are “11”
Sequence: 0100110111

## Slide 28: In-Class Exercise – One Moore Solution
A Snail is crawling across a sequence of numbers and he smiles if the last 2 numbers are “11”
Sequence: 0100110111
S1
=0
S0
=0
S3
=1
N=0
N=1
N=1
N=0
N=0
N=1
reset

## Slide 29: Homework – Review Book Example
Take a look at how the book implements “01”
Example 3.7 on p 132
A Snail is crawling across a sequence of numbers and he smiles if the last 2 numbers are “01”
Sequence: 0100110111

## Slide 30: Homework – Review Book Example
Example 3.7 on p 132
A Snail is crawling across a sequence of numbers and he smiles if the last 2 numbers are “01”
Sequence: 0100110111
Copyright © 2013 Elsevier Inc. All rights reserved.
Figure 3.30 FSM state transition diagrams: (a) Moore machine, (b) Mealy machine