## Slide 1
ECE 281
Lesson 2
1
Maj Walchko, PhD

## Slide 2: Lesson 2 Outline
Addition/Subtraction
Carry/Overflow
Negative Numbers
Logic Gates

## Slide 3: Bitbucket
Create Private Bitbucket Repository
  https://bitbucket.org/
  Name repo something like “ECE281_YourName”
  Give me access to repo. My Username: walchko
Example/Template Lab Notebook:
  http://ece.ninja/383/lab/labnotebook.html
  https://github.com/jfalkinburg/ECE_382_Lab_Ex/

## Slide 4: Simple Logic Overview
Combinational circuits are built of five basic logic gates:
AND gate - output is 1 if BOTH inputs are 1
OR gate - output is 1 if AT LEAST one input is 1
XOR gate - output is 1 if ONLY one input is 1
NAND gate - output is 1 if AT LEAST one input is 0
NOR gate - output is 1 if BOTH inputs are 0

## Slide 5: Logic Tables
These 1’s are really represented by voltage levels like 5V, 3.3V, 1.8V and 0’s are 0V

## Slide 6: Exercise
Decimal | Binary | Hexadecimal
200710 |  | 
 | 1 1011 | 
 |  | 0xDEAD

## Slide 7: Exercise
Decimal | Binary | Hexadecimal
200710 | 111 1101 0111 | 0x7D7
2710 | 1 1011 | 0x1B
5700510 | 1101 1110 1010 1101 | 0xDEAD
https://en.wikipedia.org/wiki/Hexspeak

## Slide 8: Math
Lower levels of programming (like assembly), the programmer needs to determine what the right answer is
  Higher level languages (Python, C/C++, Ruby, etc) generally take care of this automatically
  If you manipulate bits/bytes (like data through a network) you need to understand this
  Writing drivers/working close to metal
  We will talk about Arithmetic Logic Unit (ALU)
Using signed magnitude, 2’s complement, unsigned
  Pro’s/Con’s
  Addition
  Subtraction
4b ALU for the 74181 IC

## Slide 9: Number Conversions
Hex Digit | Decimal Equivalent | Binary Equivalent | Octal Equivalent
0 | 0 | 0000 | 0
1 | 1 | 0001 | 1
2 | 2 | 0010 | 2
3 | 3 | 0011 | 3
4 | 4 | 0100 | 4
5 | 5 | 0101 | 5
6 | 6 | 0110 | 6
7 | 7 | 0111 | 7
8 | 8 | 1000 | 10
9 | 9 | 1001 | 11
A | 10 | 1010 | 12
B | 11 | 1011 | 13
C | 12 | 1100 | 14
D | 13 | 1101 | 15
E | 14 | 1110 | 16
F | 15 | 1111 | 17
Copyright © 2007 Elsevier

## Slide 10: Number Conversions
Decimal | 2’s Complement | Unsigned
-3 | 1101 | 
-2 | 1110 | 
-1 | 1111 | 
0 | 0000 | 0000
1 | 0001 | 0001
2 | 0010 | 0010
3 | 0011 | 0011
Copyright © 2007 Elsevier

## Slide 11: Carry/Overflow
Overflow – Overflow occurs when the answer is too big to fit in the available number of bit
  It exceeds the range
  The answer is not the correct sign (2’s Comp)
Carry – Whenever your answer takes more than a single bit, the extra bit is a carry.
Carry and Overflow are independent
  They can occur at the same time
  One can occur without the other
  (this will probably make more sense as we continue on)
What is -5 + (- 6)?

## Slide 12: backups

## Slide 13
Figure 1.13 Buffer
Buffer

## Slide 14
Figure 1.12 NOT gate
NOT Gate

## Slide 15
Figure 1.14 AND gate
AND Gate

## Slide 16
Figure 1.15 OR gate
OR Gate

## Slide 17
Figure 1.16 More two-input logic gates
XOR, NAND, and NOR Gates

## Slide 18
Figure 1.17 XNOR gate
XNOR Gate
Figure 1.18 XNOR truth table

## Slide 19
Figure 1.19 Three-input NOR gate
Three-input NOR Gate
Figure 1.20 Three-input NOR truth table

## Slide 20
Figure 1.21 Four-input AND gate
Four-input AND Gate
Figure 1.22 Four-input AND truth table