## Slide 1
ECE 281 Lesson 21
1

## Slide 2: Lesson 21 Outline
Do Time Logs!
Lab2 Notebook Due @ 2359 Today
Sequential Building Blocks
  Counters
  Shift Registers
Memory
  RAM
  ROM

## Slide 3: N-Bit Counter

## Slide 4: Shift Register Schematic
Serial to parallel conversion
Data shifted into registers on rising clock
Once all data in place, you can read the parallel out

## Slide 5: Shift Register with Parallel Load
Parallel to serial
  Load -> high
  Mux feeds parallel data to registers
  Load -> low
  Data is shifted out

## Slide 6: Memory
Address – Indicates which row of memory is read/written (location) 2N (N-Bits)
Data – Value read/written M-Bits
Word – size of a row of data (M-Bits)
Depth – Number of rows
Width – Number of Columns
Wordline – Assert based on address to activate bit cells in a row
Bitline – kept at Z; when wordline is activated
  Driven to 1 or 0 by bit cell to read
  When written, drives bit cell high or low
Port – Gives read/write access to the address; multi-ported can read/write several addresses at the same time

## Slide 7: Memory
Registers of Flip-Flops can store small amounts of data
Memory arrays can store large amounts of data
Memory reads/writes contents of one row of the array
(Address a row)
(read or write)

## Slide 8: 3-Bit Memory Array
Width – how many bits in data … a data bus is 10 bits wide
Depth – how much data can you store?
(in)
(out)

## Slide 9: 4x3 Memory Array
(rows x columns)

## Slide 10: 32 Kb Array
32 Kb array: depth = 210 = 1024 words, width = 32 bits
1024 words of size 32b inside this memory
(in)
(out)

## Slide 11: Types of Memory
Types of memory:
  RAM –
    Random Access Memory
    Delay same for all addresses, vs sequential (e.g. type)
    Volatile – Loses its data when the power is lost
  ROM –
    Read Only Memory
    Also randomly accessed
    Some are re-writable
    Non-Volatile

## Slide 12: Types of RAM
DRAM – Dynamic RAM
  Bit stored as absence or presence of charge on a capacitor
  Reading destroys data; must be rewritten
  Must be refreshed every few miliseconds due to leaking charge

## Slide 13: DRAM Stored Values
transistor
Capacitors store 1 as charge or 0 as absence of charge
Once read, needs to be refreshed
Capacitor leakage leads to constant refreshing even if not read

## Slide 14: Types of DRAM
DRAM – Dynamic RAM
  Bit stored as absence or presence of charge on a capacitor
  Reading destroys data; must be rewritten
  Must be refreshed every few miliseconds due to leaking charge
  SDRAM – Synchronous DRAM
    Uses pipelined memory access
  DDR SDRAM – Double data rate SDRAM
    Uses Rising and falling edge to access data

## Slide 15: Types of RAM
SRAM – Static RAM
  Does not need refreshing
  Bit stored in cross coupled inverters
  Inverters can restore value if noise interferes

## Slide 16: Types of RAM
Larger memories tend to be slower
More transistors = more size, power, and cost
Best Memory depends on speed, cost, power constraints
Memory Type | Transistors per bit cell | Latency
Flip-Flop |  | 
SRAM |  | 
DRAM |  | 
Memory Type | Transistors per bit cell | Latency
Flip-Flop | ~20 | Fast
SRAM | 6 | Medium
DRAM | 1 | Slow

## Slide 17: Raspberry Pi Register Map

## Slide 18: ROM Bit Cells
Programmable ROM – Provides a way to connect transistor with ground
A way to implement, until you blow the fuse, you can read/write

## Slide 19: Types of ROM
PROM – Programmable Read Only Memory – Provides a way to connect transistor with ground
Fuse Programmable ROM – blow fuse = 1, cannot be rewritten
EPROM – Eraseable PROM
  High voltage to write
  UV light to erase
EEPROM – Electrically EPROM
  Bit cells individually erased
  Erased without UV light with extra circuitry
Flash – Large blocks erased
  Cheaper because less erasing circuitry

## Slide 20: 4-Word – 1-Bit memory array used as lookup table
Copyright © 2013 Elsevier Inc. All rights reserved.
Figure 5.52 4-word  1-bit memory array used as a lookup table

## Slide 21: 3 ROM Dot Notation
Copyright © 2013 Elsevier Inc. All rights reserved.
Figure 5.49 4  3 ROM: dot notation

## Slide 22: 3 ROM Dot Notation
Copyright © 2013 Elsevier Inc. All rights reserved.
Figure 5.49 4  3 ROM: dot notation

## Slide 23: 3 ROM Dot Notation – using gates
Copyright © 2013 Elsevier Inc. All rights reserved.
Figure 5.50 4  3 ROM implementation using gates

## Slide 24: Practice
5.43: Build a 32-Bit Synchronous Up/Down Counter
  Inputs: Reset, Up = 1 (i.e. Up)

## Slide 25
25

## Slide 26: Types of ROM
PROM – Programmable Read Only Memory – Provides a way to connect transistor with ground
Fuse Programmable ROM – blow fuse = 1, cannot be rewritten
EPROM – Eraseable PROM
  High voltage to write
  UV light to erase
EEPROM – Electrically EPROM
  Bit cells individually erased
  Erased without UV light with extra circuitry
Flash – Large blocks erased
  Cheaper because less erasing circuitry

## Slide 27: Fuse-Programmable ROM Bit Cell
Copyright © 2013 Elsevier Inc. All rights reserved.
Figure 5.51 Fuse-programmable ROM bit cell

## Slide 28: Counter Symbol
Copyright © 2013 Elsevier Inc. All rights reserved.
Figure 5.30 Counter symbol

## Slide 29: Shift Register Symbol
Copyright © 2013 Elsevier Inc. All rights reserved.
Figure 5.33 Shift register symbol

## Slide 30: Shift Register with Parallel Load
What is the difference between a Shifter and a Shift Register?
A shifter is purely combinational logic

## Slide 31: Sequential Building Blocks
What is the Difference between Sequential and Combinational Logic Circuits?
  Sequential has memory (i.e. Flip-Flops)

## Slide 32: Bit Cell
Copyright © 2013 Elsevier Inc. All rights reserved.
Figure 5.41 Bit cell

## Slide 33: DRAM Bit Cell
Copyright © 2013 Elsevier Inc. All rights reserved.
Figure 5.44 DRAM bit cell

## Slide 34: Register File
Register File – Group of registers that stores temporary variables
  Often consists of small multiported SRAM
Figure 5.47 32  32 register file with two read ports and one write port
Copyright © 2013 Elsevier Inc. All rights reserved.

## Slide 35: SRAM Bit Cell
Copyright © 2013 Elsevier Inc. All rights reserved.
Figure 5.46 SRAM bit cell