## Slide 1
ECE 281 Lesson 30
1

## Slide 2: Lesson 30 Outline
Do Time Logs!
OBJECTIVES
  Understand the 3 instruction types
  Convert assembly to machine code for all instruction types
  Machine code to assembly for all instruction types
  Addressing Modes
  Practice using your reference sheets!
  Verify results and practice assembly in MIPS simulator
K:\DF\DFEC\ECE281\Handouts and Resources\Past GRs

## Slide 3: MIPS Architecture
The MIPS Architecture consists of:
  A set of operations (instructions)
    I-Type, R-Type, J-Type
  Data units (sizes, addressing modes, etc.)
    32-Bit Data Word
  Registers
    32, 32-bit registers
  Interaction with memory
    Harvard Architecture
    Load and Store
  Program counter
    32-bit PC

## Slide 4
Single Cycle MIPS microArch

## Slide 5
MIPS Instruction Types
R-Type Instructions – Register Type
I-Type Instructions – Immediate Type
J-Type Instructions – Jump Type
J-Type | 
op | addr
6 bits | 26 bits
I-Type |  |  | 
op | rs | rt | imm
6 bits | 5 bits | 5 bits | 16 bits
R-Type |  |  |  |  | 
op | rs | rt | rd | shamt | funct
6 bits | 5 bits | 5 bits | 5 bits | 5 bits | 6 bits

## Slide 6
I-Type Instructions
I-Type |  |  | 
op | rs | rt | imm
6 bits | 5 bits | 5 bits | 16 bits
I-Type Instructions – Immediate Type
Uses 2 registers operands and 1 immediate operand
Example Assembly Instruction:
instr rt, rs, imm
instr rt, imm (rs)
Boardwork: addi $s0, $0, 4
(e.g. addi & andi)
(e.g. lw & sw)
What is the Difference between SignImm and ZeroImm?

## Slide 7
Copyright © 2013 Elsevier Inc. All rights reserved.
Figure 6.9 Machine code for I-type instructions
I-Type Instructions
addi is SignImm (sign extended) because the value could be negative

## Slide 8
Copyright © 2013 Elsevier Inc. All rights reserved.
Figure 6.10 Machine code for an l-type instruction
I-Type Instructions

## Slide 9
Copyright © 2013 Elsevier Inc. All rights reserved.
J-Type Instructions
J-Type | 
op | addr
6 bits | 26 bits
J-Type Instructions – Jump Type
j or jal (jr is an R-Type Instruction that uses only the rs operand)

## Slide 10
MIPS Memory Map
Figure 6.31 MIPS memory map
Copyright © 2013 Elsevier Inc. All rights reserved.

## Slide 11
Copyright © 2013 Elsevier Inc. All rights reserved.
J-Type Instructions
J-Type | 
op | addr
6 bits | 26 bits
Given this code convert Jump:
0x00400000 addi $s0, $0, 4 # $s0 = 4
0x00400004 addi $s1, $0, 1 # $s1 = 1
0x00400008 j target # jump to target
0x0040000c addi $s1, $s1, 1 # not executed
0x00400010 sub $s1, $s1, $s0 # not executed
target:
0x00400014 add $s1, $s1, $s0 # $s1 = 1 + 4 = 5

## Slide 12
Copyright © 2013 Elsevier Inc. All rights reserved.
Verify in MIPS MARS Simulator

## Slide 13
J-Type Instructions
# This is not a good program. It is just for practice for verifying j instruction machine code
main: addi $sp, $sp, -4
sw $ra, 0($sp)
addi $a0, $0, 2
sw $a0, 0($0) # dummy statement
addi $a1, $0, 3
sw $a1, 0($0) # dummy statement
jal sum # FIND MACHINE CODE (sum is at 0x0040002C)
sw $v0, 0($0) # dummy statement
lw $ra, 0($sp)
addi $sp, $sp, 4
jr $ra
sum: add $v0, $a0, $a1
jr $ra

## Slide 14
MIPS Instruction Types
R-Type Instructions – Register Type
I-Type Instructions – Immediate Type
J-Type Instructions – Jump Type
J-Type | 
op | addr
6 bits | 26 bits
I-Type |  |  | 
op | rs | rt | imm
6 bits | 5 bits | 5 bits | 16 bits
R-Type |  |  |  |  | 
op | rs | rt | rd | shamt | funct
6 bits | 5 bits | 5 bits | 5 bits | 5 bits | 6 bits

## Slide 15
Addressing Modes
5 Addressing Modes (MIPS only)
Register-Only
  Uses registers for all source & destination operands
  All R-Type Instructions use this mode.
Immediate
  Use 16-bit immediate & registers as operands
  Used by some I-type instructions (eg addi, lui)
Base
  Effective address of memory operand found by adding base address in rs to sign extended immediate (offset)
  Used by lw, sw, etc
  Sign vs zero extended 16-bit immediate
    6
    -6

## Slide 16
Addressing Modes Cont.
PC Relative
  What is PC? – Program counter
  Used by conditional branch instructions
  16-bit immediate is added to PC to give new PC; address is relative to current PC
  branch target address is where you branch to
  16-bits gives # instructions after next instructions (eg PC+4+imm)
  imm is calculated by processor
Pseudo-direct
  Address specified in j instruction
  4 MSBs come from PC+4
  2 LSBs are 0 because addresses are word aligned
  Jump target address calculated by PC

## Slide 17
Saving Registers on the Stack
Since MIPS doesn’t have Push, Pop, and Peek instructions:
Code Example 6.25 Function Saving Registers on the Stack
  MIPS Assembly Code
  # $s0 = result
  diffofsums:
  addi $sp, $sp, -12 # make space on stack to store three registers
  sw $s0, 8($sp) # save $s0 on stack
  sw $t0, 4($sp) # save $t0 on stack
  sw $t1, 0($sp) # save $t1 on stack
  add $t0, $a0, $a1 # $t0 = f + g
  add $t1, $a2, $a3 # $t1 = h + i
  sub $s0, $t0, $t1 # result = (f + g) - (h + i)
  add $v0, $s0, $0 # put return value in $v0
  lw $t1, 0($sp) # restore $t1 from stack
  lw $t0, 4($sp) # restore $t0 from stack
  lw $s0, 8($sp) # restore $s0 from stack
  addi $sp, $sp, 12 # deallocate stack space
  jr $ra # return to caller

## Slide 18
Practice 1
Convert the following to assembly
if (g > h)
g = g + h;
else
g = g - h;
Reference Code Example 6.10 and 6.11 for 16-bit and 32-bit constant initialization
Let $s0 = g and $s1 = h
Let’s use these instructions:
  slt rd, rs, rt if rs < rt, then rd = 1, else rd = 0
  beq rs, rt, label if rs = rt, then branch to label

## Slide 19
Practice 1 solution

## Slide 20
Practice 2
Convert the following to assembly
for (i = 0; i < 20; i++)
{
a = a + 2*i;
}
Let $s0 = i $s1 = a $t0 = 20

## Slide 21
21

## Slide 22
MIPS Instruction Types
R-Type Instructions – Register Type
I-Type Instructions – Immediate Type
J-Type Instructions – Jump Type
J-Type | 
op | addr
6 bits | 26 bits
I-Type |  |  | 
op | rs | rt | imm
6 bits | 5 bits | 5 bits | 16 bits
R-Type |  |  |  |  | 
op | rs | rt | rd | shamt | funct
6 bits | 5 bits | 5 bits | 5 bits | 5 bits | 6 bits

## Slide 23
Machine Code to Assembly
Find the Assembly Function:
Given Machine Code: 0xAD310004

## Slide 24
Copyright © 2013 Elsevier Inc. All rights reserved.
MIPS Register Set

## Slide 25
Copyright © 2013 Elsevier Inc. All rights reserved.
MIPS Instruction Set

## Slide 26
MIPS Instruction Set
Copyright © 2013 Elsevier Inc. All rights reserved.
Table B.1 Instructions, sorted by opcode

## Slide 27
MIPS Instruction Set
Copyright © 2013 Elsevier Inc. All rights reserved.
Table B.1 Instructions, sorted by opcode

## Slide 28
MIPS Instruction Set
Copyright © 2013 Elsevier Inc. All rights reserved.
Table B.2 R-type instructions, sorted by funct field

## Slide 29
MIPS Instruction Set
Copyright © 2013 Elsevier Inc. All rights reserved.
Table B.2 R-type instructions, sorted by funct field

## Slide 30
MIPS Instruction Set
Copyright © 2013 Elsevier Inc. All rights reserved.
Table B.3 F-type instructions (fop = 16/17)