## Slide 1
ECE 281 Lesson 33
1

## Slide 2: Lesson 33 Outline
Do Time Logs!
CE 5 BOC Today!
LSN 35 Lab 4 PreLab
Microarchitecture
Build I-Type Instruction
Build R-Type Instruction

## Slide 3: Primary Objective for Lessons 33, 34, and Lab 4
Demonstrate the ability to design and test a microarchitecture (datapath and control unit) to implement a simple computer architecture.

## Slide 4: Lesson 33/34 Objectives

## Slide 5
The glue that brings
it all together!
Abstraction

## Slide 6: Review
Architecture – Defined by
  Instruction set
  Architectural state (e.g., PC & 32 registers for MIPS)
Based on current arch. state, processor executes instruction with data set  next arch. state
  What does this sound like?

## Slide 7: Review
Microarchitecture…we’ll look at in two parts
  Datapath – operates on words of data
    includes memories, registers, ALU, muxes, etc.
    How many bits for MIPS datapath?
  Control – get current instruction from datapath and tells datapath how to execute

## Slide 8
Computer Block Diagram
CPU
Control
Datapath
ALU
Memory
Input/
Output
Control Bus
Data Bus
Address Bus
Outside
World

## Slide 9
Multiple MIPS microarchitectures
Single cycle
Multi-cycle
Pipelined

## Slide 10
Copyright © 2013 Elsevier Inc. All rights reserved.
Complete Single-Cycle MIPS Processor
Figure 7.11 Complete single-cycle MIPS processor
Control Unit - Next Lesson
Datapath

## Slide 11: Review
Microarchitecture…we’ll look at in two parts
  Datapath – operates on words of data
    includes memories, registers, ALU, muxes, etc.
    How many bits for MIPS datapath?
  Control – get current instruction from datapath and tells datapath how to execute
Instructions we’ll implement in examples
  R-type arithmetic/logic: add, sub, and, or, slt
  Memory: lw, sw
  Branches: beq

## Slide 12: Design Process - Datapath
Start with H/W for state elements (memory and arch. state)
Add blocks of combinatorial logic between state elements
  New state computed on current state
  Again, like creating a giant Moore FSM!
Need HW to support all 5 addressing modes:
  Register Only (r-types)
  Immediate (some i-types: addi, lui, etc)
  Base (base addr + signed ext imm (offset), eg lw, sw, etc)
  PC relative (conditionals)
  Pseudo-direct (jumps)

## Slide 13
Copyright © 2013 Elsevier Inc. All rights reserved.
State Elements of MIPS
Processor
Figure 7.1 State elements of MIPS processor
Instruction Memory – put in address get out data
Register File – can do two reads at once
  A1  RD1 A2  RD2
  A3  WD3 and is Controlled by WE
Data Memory – put in address, controlled by WE
ROM

## Slide 14: ALU
F2:0 | Function
000 | A & B
001 | A ¦ B
010 | A + B
011 | not used
100 | A & ~B
101 | A ¦ ~B
110 | A - B
111 | SLT

## Slide 15: I-Type Instruction lw rt, imm(rs)
I-Type |  |  | 
op | rs | rt | imm
6 bits | 5 bits | 5 bits | 16 bits
31:26 | 25:21 | 20:16 | 15:0
Let’s try this:
lw rt, imm(rs)
We are going to write to rt: [rt] = [addr] = [rs +/- sigImm]

## Slide 16
Copyright © 2013 Elsevier Inc. All rights reserved.
I-Type Instruction
lw rt, imm(rs)
Step 1:
Figure 7.2 Fetch instruction from memory
I-Type |  |  | 
op | rs | rt | imm
6 bits | 5 bits | 5 bits | 16 bits
31:26 | 25:21 | 20:16 | 15:0

## Slide 17
Copyright © 2013 Elsevier Inc. All rights reserved.
I-Type Instruction
lw rt, imm(rs)
Figure 7.3 Read source operand from register file
Step 2:
I-Type |  |  | 
op | rs | rt | imm
6 bits | 5 bits | 5 bits | 16 bits
31:26 | 25:21 | 20:16 | 15:0

## Slide 18
Copyright © 2013 Elsevier Inc. All rights reserved.
I-Type Instruction
lw rt, imm(rs)
Figure 7.4 Sign-extend the immediate
Step 3:
I-Type |  |  | 
op | rs | rt | imm
6 bits | 5 bits | 5 bits | 16 bits
31:26 | 25:21 | 20:16 | 15:0

## Slide 19
Copyright © 2013 Elsevier Inc. All rights reserved.
I-Type Instruction
lw rt, imm(rs)
Figure 7.5 Compute memory address
Step 4:
I-Type |  |  | 
op | rs | rt | imm
6 bits | 5 bits | 5 bits | 16 bits
31:26 | 25:21 | 20:16 | 15:0
F2:0 | Function
000 | A & B
001 | A ¦ B
010 | A + B
011 | not used
100 | A & ~B
101 | A ¦ ~B
110 | A - B
111 | SLT

## Slide 20
Copyright © 2013 Elsevier Inc. All rights reserved.
I-Type Instruction
lw rt, imm(rs)
Figure 7.6 Write data back to register file
Step 5:
I-Type |  |  | 
op | rs | rt | imm
6 bits | 5 bits | 5 bits | 16 bits
31:26 | 25:21 | 20:16 | 15:0

## Slide 21
Copyright © 2013 Elsevier Inc. All rights reserved.
Determine address of next Instruction for PC
Figure 7.7 Determine address of next instruction for PC
Step 6:
I-Type |  |  | 
op | rs | rt | imm
6 bits | 5 bits | 5 bits | 16 bits
31:26 | 25:21 | 20:16 | 15:0

## Slide 22
I-Type Instruction
Enhancements for SW
I-Type |  |  | 
op | rs | rt | imm
6 bits | 5 bits | 5 bits | 16 bits
31:26 | 25:21 | 20:16 | 15:0
How about this:
sw rt, imm(rs)
Store word in memory: [rt] = [addr] = [rs +/- sigImm]

## Slide 23
R-Type Instructions
R-Type Instructions – Register Type
R-Type |  |  |  |  | 
op | rs | rt | rd | shamt | funct
6 bits | 5 bits | 5 bits | 5 bits | 5 bits | 6 bits
R-Type |  |  |  |  | 
op | rs | rt | rd | shamt | funct
6 bits | 5 bits | 5 bits | 5 bits | 5 bits | 6 bits
31:26 | 25:21 | 20:16 | 15:11 | 10:6 | 5:0
Let’s try this:
Add: [rd] = [rs] + [rt]
We are going to add 2 numbers together

## Slide 24: R-Type Instructions add rd, rs, rt
R-Type |  |  |  |  | 
op | rs | rt | rd | shamt | funct
6 bits | 5 bits | 5 bits | 5 bits | 5 bits | 6 bits
31:26 | 25:21 | 20:16 | 15:11 | 10:6 | 5:0
R-Type |  |  |  |  | 
op | rs | rt | rd | shamt | funct
6 bits | 5 bits | 5 bits | 5 bits | 5 bits | 6 bits
31:26 | 25:21 | 20:16 | 15:11 | 10:6 | 5:0

## Slide 25
Copyright © 2013 Elsevier Inc. All rights reserved.
Datapath Enhancements for
R-Type Instruction
Figure 7.9 Datapath enhancements for R-type instruction
R-Type |  |  |  |  | 
op | rs | rt | rd | shamt | funct
6 bits | 5 bits | 5 bits | 5 bits | 5 bits | 6 bits
31:26 | 25:21 | 20:16 | 15:11 | 10:6 | 5:0
Steps for R-Type Instructions
(ex ADD: add rd, rs, rt):
Read 2 Registers
Do ALU Op
Write/Register
Add a Destination

## Slide 26
Datapath Enhancements for
BEQ Instruction
Now, let’s look at a BEQ, what do we have to change here?
beq rs, rt, label
if([rs] == [rt]) PC = BTA BTA is branch target address

## Slide 27
Copyright © 2013 Elsevier Inc. All rights reserved.
Complete Single-Cycle MIPS Processor
Figure 7.11 Complete single-cycle MIPS processor
Control Unit - Next Lesson

## Slide 28
Single-Cycle Processor
Three weaknesses of Single-Cycle Processor:
  Needs clock cycle long enough for slowest instruction (lw)
  Needs 3 adders (i.e. more $$$)
  Separate instruction and data memory (not always realistic)
Recall: Multiple microarchitectures for a single architecture
MIPS:
  Single-Cycle
  Multi-Cycle
  Pipelined

## Slide 29
Single-Cycle MIPS Processor
All executed in one cycle (i.e. single-cycle MIPS)
 Assuming no memory delay

## Slide 30
30

## Slide 31: MIPS Memory Map
Figure 6.31 MIPS memory map
$sp = 0x7FFFFFFC
Reserved
Reserved
Dynamic Data
Stack
Heap
$gp = 0x10008000
Global Data
PC = 0x00400000
Text

## Slide 32: Steps for Translating and starting a program
Compiler
Assembler
Higher Level Language (HLL)
Assembly Language
Object File (Machine Code)
Linker
Executable
Loader
Memory
Object Files
Library Files

## Slide 33
Copyright © 2013 Elsevier Inc. All rights reserved.
MIPS Register Set

## Slide 34
Copyright © 2013 Elsevier Inc. All rights reserved.
MIPS Instruction Set

## Slide 35
MIPS Instruction Set
Copyright © 2013 Elsevier Inc. All rights reserved.
Table B.1 Instructions, sorted by opcode

## Slide 36
MIPS Instruction Set
Copyright © 2013 Elsevier Inc. All rights reserved.
Table B.1 Instructions, sorted by opcode

## Slide 37
MIPS Instruction Set
Copyright © 2013 Elsevier Inc. All rights reserved.
Table B.2 R-type instructions, sorted by funct field

## Slide 38
MIPS Instruction Set
Copyright © 2013 Elsevier Inc. All rights reserved.
Table B.2 R-type instructions, sorted by funct field

## Slide 39
MIPS Instruction Set
Copyright © 2013 Elsevier Inc. All rights reserved.
Table B.3 F-type instructions (fop = 16/17)

## Slide 40
I-Type Instructions
I-Type Instructions – Immediate Type
I-Type |  |  | 
op | rs | rt | imm
6 bits | 5 bits | 5 bits | 16 bits
I-Type |  |  | 
op | rs | rt | imm
6 bits | 5 bits | 5 bits | 16 bits
31:26 | 25:21 | 20:16 | 15:0