## Slide 1
ECE 281 Lesson 6
1
Maj Kevin Walchko

## Slide 2: Multiplexers
Implement the following using
  An 8:1 mux
  A 4:1 mux (plus an inverter for TT)
  A 2:1 mux (plus 2 other gates for TT; plus OR and inv for eqn)

## Slide 3: K-map Example
 | CD |  |  |  |  |  |  |  | 
AB |  | 00 |  | 01 |  | 11 |  | 10 | 
 | 00 | 0 |  | 1 |  | 3 |  | 2 | 
 |  | 1 |  | 1 |  | X |  | 1 | 
 | 01 | 4 |  | 5 |  | 7 |  | 6 | 
 |  | X |  | 0 |  | 0 |  | 0 | 
 | 11 | 12 |  | 13 |  | 15 |  | 14 | 
 |  | 0 |  | 1 |  | 1 |  | 1 | 
 | 10 | 8 |  | 9 |  | 11 |  | 10 | 
 |  | 1 |  | X |  | 1 |  | 1 | 
A | B | C | D | F
0 | 0 | 0 | X | 1
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | X
0 | 1 | 0 | 0 | X
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | X | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | X
1 | 0 | 1 | X | 1
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | X | 1
Note: the X’s (don’t care) makes this table shorter
You can wrap around all 4 corners, but not needed in this case
F = B’+AC+AD

## Slide 4: K-map Example
F(A, B, C, D) = ∑(0,2,4, 6, 7, 8, 10, 11, 12, 15)
  don’t care ∑(14)
 | CD |  |  |  |  |  |  |  | 
AB |  | 00 |  | 01 |  | 11 |  | 10 | 
 | 00 | 0 |  | 1 |  | 3 |  | 2 | 
 |  | 1 |  | 0 |  | 0 |  | 1 | 
 | 01 | 4 |  | 5 |  | 7 |  | 6 | 
 |  | 1 |  | 0 |  | 1 |  | 1 | 
 | 11 | 12 |  | 13 |  | 15 |  | 14 | 
 |  | 1 |  | 0 |  | 1 |  | X | 
 | 10 | 8 |  | 9 |  | 11 |  | 10 | 
 |  | 1 |  | 0 |  | 1 |  | 1 | 
4
F = D’+BC+AC

## Slide 5: Multiplexer
Example: I have 2 binary sensors (True/False) but only one input pin available to my processor, this allows me to connect to more inputs (this is a silly example at 2:1). 8:1 mux costs me 3 address lines and 1 input pin (4 pins total, but I can read 8 things) … better example.
 | BA |  |  |  |  |  |  |  | 
 | S | 00 |  | 01 |  | 11 |  | 10 | 
 | 0 | 0 |  | 1 |  | 3 |  | 2 | 
 |  | 0 |  | 1 |  | 1 |  | 0 | 
 | 1 | 4 |  | 5 |  | 7 |  | 6 | 
 |  | 0 |  | 0 |  | 1 |  | 1 | 
S | B | A | Z
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
D0
D1
You can also see this
Z = S’A+SB
Multiplexer: 2-to-1 or 2:1 shown below … basically you can switch between different inputs

## Slide 6: 74HC4067 16:1 Multiplexer
output
Selection bits
Selection bits
Inputs 8-15
Inputs 0-7
We will eventually building this chip in software using VHDL

## Slide 7: Multiplexers
Figure 2.58 4:1 multiplexer implementations: (a) two-level logic, (b) tristates, (c) hierarchical

## Slide 8: Multiplexers
Implement the following using
  An 8:1 mux
  A 4:1 mux (plus an inverter for TT)
  A 2:1 mux (plus 2 other gates for TT; plus OR and inv for eqn)
A | B | C | Y
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1

## Slide 9: 8:1 Mux
A | B | C | Y
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
If an Y is 1, then it is connected to VCC and if Y is 0, then it is connected to GND.
000
001
010
011
100
101
110
111
VCC
GND
ABC
3
Y

## Slide 10: 4:1 Mux
A | B | C | Y
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
B | C | Y
0 | 0 | A’
0 | 1 | 0
1 | 0 | 1
1 | 1 | 1
00
01
10
11
VCC
GND
Y
A
BC
2
We can simplify this down by removing the MSB and looking at the other remaining inputs. There is a pattern we can exploit.

## Slide 11: 2:1 Mux
A | B | C | Y
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
B | Y
0 | A’C’
1 | 1
Now looking at the 4:1 TT, we see B follows Y closer than C, so let’s remove C.
B | C | Y
0 | 0 | A’
0 | 1 | 0
1 | 0 | 1
1 | 1 | 1
Original
0
1
VCC
Y
C
B
1
A

## Slide 12: Decoder
Figure 2.63 2:4 decoder

## Slide 13: 2:4 Decoder - VHDL
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
entity decode_2to4 is
Port (A : in STD_LOGIC_VECTOR (1 downto 0); -- 2-bit input
EN : in STD_LOGIC; -- enable input
Y : out STD_LOGIC_VECTOR (3 downto 0)); -- 4-bit output
end decode_2to4;
architecture Behavioral of decode_2to4 is
begin
Y(0) <= '1' when A = "00" else
'0';
Y(1) <= '1' when A = "01" else
'0';
Y(2) <= '1' when A = "10" else
'0';
Y(3) <= '1' when A = "11" else
'0';
end Behavioral;
Just like the Mux, we can do a decoder in VHDL
Import libraries
Define ports
code

## Slide 14: Delays
Why are there delays in a circuit?
  Capacitive Charging
  Speed of light
  Temperature
  Many inputs/outputs
Measured in ps or ns
Often listed on datasheets

## Slide 15: Vocabulary
Rising Edge – transition from low to high
Falling Edge – transition from high to low
Propagation Delay (tpd) – max time from when input changes to when output reaches final value
Contamination Delay (tcd) – min time from when input changes to when output starts changing
Critical Path – longest (slowest) path from an input to an output (i.e. Circuit tpd)
Short Path – shortest (fastest) path from an input to an output (i.e. Circuit tcd)
Glitch – Single input transition that causes multiple output transitions.

## Slide 16
Figure 2.66 Circuit delay
Delay

## Slide 17
Figure 2.67 Propagation and contamination delay
Propagation Delay and Contamination Delay

## Slide 18: Delay – Example 1
 | tpd (ps) | tcd (ps)
NOT | 15 | 10
AND | 30 | 25
OR | 40 | 35
NOR | 30 | 25
Critical Path:
Longest Path = (D)
Length = 15+30+40+30=115ps
Shortest Path:
- Shortest Path = (B)
Length = 25+25=50ps
25
25
15
30
40
30

## Slide 19: Glitch
We expect a valid output between 50ps and 115ps
What happens between 50ps and 115ps?
Glitch – Single input transition that causes multiple output transitions.
Let’s see it in action

## Slide 20: Delay – Example 2 - Glitches
B | 
BC | 
Y | 
B | 
BC | 
Y | 
0
1
1
0
1
0
1
A’B’
BC
1
1
0
1
1
0
0
AND gates are slower
0-1
Both inputs to Y are now 0, so Y changes to 0
Now one of them is 1, so Y heads back to 1

## Slide 21: Delay – Example 2 - Glitches
 | BA |  |  |  |  |  |  |  | 
 | S | 00 |  | 01 |  | 11 |  | 10 | 
 | 0 | 0 |  | 1 |  | 3 |  | 2 | 
 |  | 1 |  | 1 |  | 1 |  | 0 | 
 | 1 | 4 |  | 5 |  | 7 |  | 6 | 
 |  | 0 |  | 0 |  | 1 |  | 0 | 
To fix the glitch we can just circle the transition point and add another term and it only costs us a little circuitry.

## Slide 22: Glitches
Do we like fixing glitches?
  No, not really
  Plus, you may not fix all glitches
  Simultaneous transition on multiple inputs can cause glitches that can’t be solved by hardware
How do we eliminate glitches?
  Calculate all propagation delays for a circuit and ensure we don’t expect the result before this time.
  Often we will create a synchronous circuit (something we will learn later) with a register to store the result when it is available
Problem 2.29 from Homework…are there glitches???

## Slide 23
23

## Slide 24: Lesson 6 Outline
Do Time Logs!
Homework from last time:
  Problems 2.41 and 2.42
Review K-Maps, Multiplexers, and Decoders
Delays
Critical Path
Glitches
Due Next Time:
  CE2
  HW2 (Pre-ICE)

## Slide 25: 4:1 Mux - VHDL
library IEEE; -- These lines are similar to a #include in C
use IEEE.STD_LOGIC_1164.ALL;
entity mux_4to1 is
Port ( SEL : in STD_LOGIC_VECTOR (1 downto 0);-- select input
D : in STD_LOGIC_VECTOR (3 downto 0); -- inputs
Y : out STD_LOGIC);
end mux_4to1;
architecture Behavioral of mux_4to1 is
begin
-- These statements are called concurrent signal assignments.
-- They all happen at the same time unlike a regular programming language
Y <= D(0) when (SEL = "00") else
D(1) when (SEL = "01") else
D(2) when (SEL = "10") else
D(3) when (SEL = "11") else A(0);
end Behavioral;
Figure 2.57 4:1 multiplexer
CE 2 will start to introduce you to VHDL

## Slide 26: Delay – Example 2 - Glitches
B | 
BC | 
Y | 
B | 
BC | 
Y | 
0
1
1
10
1 is the expected output. If doesn’t transition fast enough the output may briefly be 0