## Slide 1
ECE 281 Lesson 17
1
Maj Jeffrey Falkinburg USAFA/DFEC
Room 2E46E 333-9193

## Slide 2: Lesson 17 Outline
Do Time Logs!
Do Feedback!
Homework #2 (LSN 15/16 Worksheet) – Due Now!
Lab #2 Prelab Due LSN 19!
VHDL – Sequential Logic
  Process

## Slide 3: VHDL – What we have talked about
Entity – Defines inputs and outputs of box
Architecture – Describes what is inside the box
Two Types of Architecture:
  Behavioral – Describes what module does in terms of the relationships between inputs and outputs
  Structural – Describes what a module does in terms of how it is composed of simpler modules

## Slide 4: Flip-Flops and Finite State Machines
Flip Flops Create Memory
On the Clock Edge!
Copyright © 2013 Elsevier Inc. All rights reserved.
Figure 3.20 Flip-flop current state and next state

## Slide 5: Finite State Machines – Design/Analysis
State Machines:
  0) Description
  1) State Transition Diagram
  2) State Transition Table & Output Table
  3) Next State and Output State Equations
  4) Schematic
Copyright © 2013 Elsevier Inc. All rights reserved.
Design
Analysis

## Slide 6: Finite State Machines - Moore vs Mealy Machine
Moore Machine – outputs depend only on current state of the machine.
Mealy Machine – outputs depend on both the current state and current inputs of the machine.
Combinational Logic or
Next State Logic
Flip Flops
Output Logic
Inputs
Outputs
Current
State
Next
State
Clock
M
K
K
N
Combinational Logic or
Next State Logic
Flip Flops
Output Logic
Inputs
Outputs
Current
State
Next
State
Clock
M
K
K
N

## Slide 7: Process
Process – Collection of sequential statements that execute in parallel with other concurrent statements and other processes
  Always running or suspended
  Creates a “box” that listens for signals (wires)
  When the signal changes the box is told to run
  *** Processes are scary!
    Add memory
    Make circuit hard to visualized
 If you want a Flip-Flop you need a process

## Slide 8: Generic Example Process
process(signal name, signal name, …., signal name)
Type declarations
Variable declarations
Constant declarations
Functions declarations
Procedure definitions
begin
sequential statement
…
sequential statement
end process;

## Slide 9: Specific Example Process
Specific Example Process:
process(A, B)
begin
Y <= A and B;
end process;
What do we get?

## Slide 10: No Process
What if we have assignments not in a process:
    Y <= A or C;
    Y <= A and B;
    Y <= C and D;
What do we get?

## Slide 11: Make a Process
So we make a process:
process( )
begin
    Y <= A or C;
    Y <= A and B;
    Y <= C and D;
end process;
What do we get?
A, B, C, D
Things are scheduled
Rest of stuff is ignored
Y is never assigned the first two values
Schedule is overwritten

## Slide 12: Rules for Processes
Rules for Processes:
  Think before using variables (don’t use them if you can help it)
  Avoid “innovative” use of language constructs
  *Avoid overriding a signal in a process (don’t assign a value twice)
  *Only use processes for sequential circuits
* Indicates a rule for this class only

## Slide 13: If Statements
If Statements
if boolean expression then
sequential statement
elsif boolean expression then
sequential statement
…
elsif boolean expression then
sequential statement
elsif executed only if boolean
expression true and previous
boolean expressions were false

## Slide 14: Flip-Flop Example
Flip-Flop Example
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
entity Flip_Flop is
Port ( clk, D : in STD_LOGIC;
Q : out STD_LOGIC);
end Flip_Flop;
architecture Behavioral of Flip_Flop is
begin
process(clk)
begin
if (rising_edge(clk)) then
Q <= D;
end if;
end process;
end Behavioral;
Note: Do not use
*** clk’event and clk = ‘1’
Only use rising_edge(clk)
 can only use if inside a process
Build stuff
Runs when clk changes
Only when 01
 Memory
How do we make a Latch:
if (clk = '0') then
Q <= D;
end if;

## Slide 15: Processes
Process may not declare signals, but can use variables
  Keeps track of state within a process and is not visible outside of process (i.e. local variable)
  Assign values based on a Blocking Statement
    := instead of <=
Blocking Statement
  Evaluated in order in which they appear, like in code
NonBlocking Assignments are evaluated concurrently
  Signals updated afterwards

## Slide 16: Blocking Statement Example
process(A, B)
variable tmp : STD_LOGIC;
begin
tmp := '0';
tmp := tmp or A;
tmp := tmp or B;
Y <= tmp;
end process;

## Slide 17: NonBlocking Statement Example
process(A, B)
variable tmp : STD_LOGIC;
begin
tmp <= '0';
tmp <= tmp or A;
tmp <= tmp or B;
Y <= tmp;
end process;

## Slide 18: In Class Exercise #1:
Write an HDL Module for a JK Flip Flop:
Inputs: J, K, Clk
Output: Q
  ↑  Q Keeps old value if J=K=0
  Q = 1 if J=1
  Q = 0 if K=1
  if J=K=1 (i.e. Toggle)
J | K | CLK |  |  | Comment
0 | 0 | ↑ |  |  | Latch
0 | 1 | ↑ | 0 | 1 | Reset
1 | 0 | ↑ | 1 | 0 | Set
1 | 1 | ↑ |  |  | Toggle
X | X | All others |  |  | No Change
J | K | CLK |  |  | Comment
0 | 0 | ↑ |  |  | Latch
0 | 1 | ↑ | 0 | 1 | Reset
1 | 0 | ↑ | 1 | 0 | Set
1 | 1 | ↑ |  |  | Toggle
X | X | All others |  |  | No Change

## Slide 19: In Class Exercise #2:
Write an HDL Module for a SR Latch:
Inputs: S, R
Output:
Copyright © 2013 Elsevier Inc. All rights reserved.
Figure 3.5 SR latch truth table

## Slide 20: Example Process
process(clk)
begin
if(rising_edge(clk)) then
if(reset='0') then
old_button <= "00000";
else
btnActivity <= (old_button xor btn) and btn;
end if;
old_button <= btn;
end if;
end process;

## Slide 21: Extra Instruction (EI)
Maj Jeffrey Falkinburg
2E46E
Office: 333-9193
Sometimes Available
Available
Always Unavailable
M1
ECE 281 – 2F44
M6
ECE 383 – 2E48A
M7
ECE 383 – 2E48A
M5
T1
T5
T6
T7
M3
ECE 463 – 2G2
M4
ECE 463 – 2G2
T2
M2
ECE 281 – 2F44
T3
ECE 383 – 2E48A
T4
ECE 383 – 2E48A

## Slide 22
22