## Slide 1
ECE 281 Lesson 18
1
Maj Jeffrey Falkinburg USAFA/DFEC
Room 2E46E 333-9193

## Slide 2: Lesson 18 Outline
Do Time Logs!
Lab 2 Prelab Due BOC LSN 19!
Review
State Machines
ICE

## Slide 3: Blocking Statement Example
process(A, B)
variable tmp : STD_LOGIC;
begin
tmp := '0';
tmp := tmp or A;
tmp := tmp or B;
Y <= tmp;
end process;

## Slide 4: NonBlocking Statement Example
process(A, B)
signal tmp : STD_LOGIC;
begin
tmp <= '0';
tmp <= tmp or A;
tmp <= tmp or B;
Y <= tmp;
end process;

## Slide 5: In Class Exercise #1:
Write an HDL Module for a JK Flip Flop:
Inputs: J, K, Clk
Output: Q
  ↑  Q Keeps old value if J=K=0
  Q = 1 if J=1
  Q = 0 if K=1
  if J=K=1 (i.e. Toggle)
J | K | CLK |  |  | Comment
0 | 0 | ↑ |  |  | Latch
0 | 1 | ↑ | 0 | 1 | Reset
1 | 0 | ↑ | 1 | 0 | Set
1 | 1 | ↑ |  |  | Toggle
X | X | All others |  |  | No Change
J | K | CLK |  |  | Comment
0 | 0 | ↑ |  |  | Latch
0 | 1 | ↑ | 0 | 1 | Reset
1 | 0 | ↑ | 1 | 0 | Set
1 | 1 | ↑ |  |  | Toggle
X | X | All others |  |  | No Change

## Slide 6: VHDL – What we have talked about
Entity – Defines inputs and outputs of box
Architecture – Describes what is inside the box
Two Types of Architecture:
  Behavioral – Describes what module does in terms of the relationships between inputs and outputs
  Structural – Describes what a module does in terms of how it is composed of simpler modules

## Slide 7: Flip-Flops and Finite State Machines
Flip Flops Create Memory
On the Clock Edge!
Copyright © 2013 Elsevier Inc. All rights reserved.
Figure 3.20 Flip-flop current state and next state

## Slide 8: Finite State Machines – Design/Analysis
State Machines:
  0) Description
  1) State Transition Diagram
  2) State Transition Table & Output Table
  3) Next State and Output State Equations
  4) Schematic
Copyright © 2013 Elsevier Inc. All rights reserved.
Design
Analysis

## Slide 9: Finite State Machines - Moore vs Mealy Machine
Moore Machine – outputs depend only on current state of the machine.
Mealy Machine – outputs depend on both the current state and current inputs of the machine.
Combinational Logic or
Next State Logic
Flip Flops
Output Logic
Inputs
Outputs
Current
State
Next
State
Clock
M
K
K
N
Combinational Logic or
Next State Logic
Flip Flops
Output Logic
Inputs
Outputs
Current
State
Next
State
Clock
M
K
K
N

## Slide 10: State Machines
Draw State Machine for Stoplight
Combinational Logic or
Next State Logic
Flip Flops
Output Logic
Inputs
Outputs
Current
State
Next
State
Clock
M
K
K
N

## Slide 11: Enumerate Data Types
type sm_stoplight is (s_red, s_green, s_yellow);
signal next_state, current_state : sm_stoplight;

## Slide 12: Next State Flip Flop
process (clk, reset)
begin
  if reset = '1' then
  current_state <= s_yellow;--Reset state
  elsif (rising_edge(clk)) then
  current_state <= next_state;--Next state becomes current state
  end if;
end process;

## Slide 13: Case Statements
process (current_state,–- Other sensitive inputs)
begin
  case current_state is
    when state1=>
      -- Sequential Statements
    when state2 =>
      -- Sequential Statements
    when state3 =>
      -- Sequential Statements
    when others =>
      -- Sequential Statements
  end case;
end process;

## Slide 14: Case Statements – 7SD (combinatorial***)
Selected signal assignments would work just as well…
Important!***

## Slide 15: Testbenches
Assert (check output)
Report (report message)
Severity (Error, Warning, Note, Failure)
A <= '0'; B <= '0'; C <= '0'; D <= '0' ; S <= "00";
wait for 10 ns;
ASSERT Y = '1' REPORT "Test 0000 00 Failed" SEVERITY ERROR;
-- Can use Error, Warning, Note Failure
Be Careful with its use: What could be an issue?
  Propagation Delay

## Slide 16: Component Declaration and Instantiation
How Many of you have investigated your testbenches?
Declaration: In Architecture…Before Begin (Make Known)
  component Component_Name
    port ( -- signal_name : mode signal_type;
    Input0, Input1 : in std_logic;
    Output :out std_logic);
  end component;
Instantiation: In Architecture…After Begin (Component Used)
Component_Label: Component_Name
  port map ( -- Port_name => Signal name,
  Input0 => a,
  Input1 => b,
  Output => Y);

## Slide 17: Divide-by-3 Counter – Example 3.6
The waveform and state transition diagram for a divide-by-3 counter is shown in Figure 3.28
Next State Table | 
Current State | Next State
S0 | S1
S1 | S2
S2 | S0
Output Table | 
Current State | Output
S0 | 1
S1 | 0
S2 | 0

## Slide 18: Divide-by-3 Counter – Example 3.6
Next State Table | 
Current State | Next State
S0 | S1
S1 | S2
S2 | S0
Output Table | 
Current State | Output
S0 | 1
S1 | 0
S2 | 0

## Slide 19: Homework – Review Book Example
Take a look at how the book implements “01”
Example 3.7 on p 132
A Snail is crawling across a sequence of numbers and he smiles if the last 2 numbers are “01”
Sequence: 0100110111

## Slide 20: Homework – Review Book Example

## Slide 21: Homework – Review Book Example

## Slide 22: Extra Instruction (EI)
Maj Jeffrey Falkinburg
2E46E
Office: 333-9193
Sometimes Available
Available
Always Unavailable
M1
ECE 281 – 2F44
M6
ECE 383 – 2E48A
M7
ECE 383 – 2E48A
M5
T1
T5
T6
T7
M3
ECE 463 – 2G2
M4
ECE 463 – 2G2
T2
M2
ECE 281 – 2F44
T3
ECE 383 – 2E48A
T4
ECE 383 – 2E48A

## Slide 23
23